## Slide 1: Performance measures

## Slide 2: Machine balance
Computation
  peak performance
  double precision FLOPS/s (FLOating point OPerationS per second)
Memory access
  bandwidth
  Gwords/s per gigawords per second
Machine balance

## Slide 3: Code balance
Computation
  number of FLOPS
Memory access
  number of word load and store operations
Code balance
Computational intensity

## Slide 4: Light speed
Expected fraction of peak performance
Light speed
  < 1: memory bound, i.e., bandwidth limited
  = 1: compute bound
Expected performance (GFLOPS/s)
P =

## Slide 5: Example
Machine balance for dual socket Intel Xeon E5-2680v4 @ 2.40GHz (broadwell, AVX2)
  peak performance: 4 dp × 2.4∙109 FLOPS/s × 14 × 2 = 269 GFLOPS/s
  memory bandwidth: 125 GB/s (vector triad)
  Machine balance Bm = 0.46 bytes/FLOP
Code balance for vector triad
  FLOPS: 1 add + 1 multiply = 1 FLOP
  Data transfer: 2 loads + 1 store = 4 transfers
  Code balance Bc = 4 transfers/FLOP
Light speed = 0.11
Performance = 31 GFLOPS/s
double a[n], b[n], c[n],
s;
…
for (i = 0; i < n; i++)
a[i] = b[i] + s*c[i];